## Slide 1
AI Solutions for Vessel Identification in SAR Images
LOOKING FOR VESSELS DETECTION?
Zazzarini Micol – Fiorani Andrea

## Slide 2
SAR Ship Detection
State of Art
Materials and Methods
Hyperparameter Tuning
Optimization
Conclusion
Contents

## Slide 3
Problem: Identification of objects at sea using SAR for the monitoring and surveillance of vessels in absence of AIS signal.
Our Goal: improve the current state of the art in vessel identification using Synthetic Aperture Radar (SAR) imagery, in collaboration with National Research Council of Italy (CNR)
SAR Ship Detection

## Slide 4
Understanding SAR Technology
Exploring the role of Synthetic Aperture Radar in Maritime Surveillance
Definition of SAR
Synthetic Aperture Radar
SAR is a remote sensing method used to create images of objects on the ground, including vessels at sea.
2) Vessel Detection
SAR technology effectively detects and monitors vessels, making it essential for maritime operations and surveillance.
3) High-Resolution Imagery
SAR provides detailed images regardless of weather conditions, ensuring reliable and accurate monitoring day and night.
4) Radar Reflection Analysis
Analysis of radar reflections from ship structures enables precise identification and tracking of various vessels.
5) Applications in Surveillance
Crucial for detecting illegal fishing and other maritime activities, SAR enhances security in dense environments.

## Slide 5
Understanding SAR Technology
Exploring the role of Synthetic Aperture Radar in Maritime Surveillance
Key Benefits of SAR Ship Detection
Exploring the Advantages of Synthetic Aperture Radar in Maritime Surveillance
Synthetic-aperture Radar
SAR technology captures detailed images, improving detection accuracy for vessels.
All-Weather Operation
Functions effectively regardless of weather conditions, ensuring reliable monitoring.
Continuous Monitoring
Allows for real-time surveillance, facilitating swift responses to illegal activities.
Cost-Effective Solution
Offers a budget-friendly option for monitoring extensive maritime areas efficiently.
Monitoring IUU Fishing
SAR can detect vessels involved in illegal fishing 24/7, even in poor weather or darkness.

## Slide 6
Understanding SAR Technology
State of Art
Traditional Algorithms
Deep Learning Algorithms
Affected by a series of limitations
One stage detectors
(YOLO)
(RCNN)
Two stage detectors

## Slide 7
Materials and Methods
Dataset
Architectures

## Slide 8
SAR Dataset of Ship Detection for Deep Learning under Complex Backgrounds
Object detectors archieve higher mean average precision on it and have higher generalization performance.
102 Chinese Gaofen-3 images and 108 Sentinel-1 images, 43.819 ship chips in total.
70%
15%
15%
Balance and consistency between images and labels

## Slide 9
SAR Dataset of Ship Detection for Deep Learning under Complex Backgrounds
Challenges
These ships have distinct scales and backgrounds, and they vary in terms of polarization, resolution, incidence angle, imaging mode, and background.
Ships appear as bright pixels mainly due to the double reflection of pulses emitted by the sensor.
The incidence angle influences the geometry of the ships, producing foreshortening, layover, and shadowing.

## Slide 10
SAR Dataset of Ship Detection for Deep Learning under Complex Backgrounds
Labeling Procedure
1. All SAR images are converted to sigma0 values
2. Candidate subimages containing ships with sizes greater than 800 pixels are cropped
3. Sliding windows from these candidate subimages are used to acquire ship images 256 x 256 pixels in size
4. They are labeled by SAR experts with LabelImg

## Slide 11
Multiscale Ships Size
PROBLEM
Compared with those objects in the optical dataset, the ship size is small, they miss the characteristics of ships on the feature map, making it difficult to distinguish ships leading to false alarms.
SOLUTION
Land-ocean segmentation
Complex backgrounds
Relative bounding box size
SAR Dataset of Ship Detection for Deep Learning under Complex Backgrounds

## Slide 12
SAR Dataset of Ship Detection for Deep Learning under Complex Backgrounds
Experimental results from « A SAR Dataset of Ship Detection for Deep Learning under Complex Backgrounds » by Wang, Zhang, Wei
The models trained on these data can detect multiscale ships with low numbers of false positives under complex backgrounds.

## Slide 13
YOLOv8 architecture
Backbone
Neck
Head

## Slide 14
YOLOv8 architecture
Head
Detect
Detect
Detect
Small Objects
Medium Objects
Big Objects
The Head manages the final object detection phase.
YOLOv8’s Key feature: division of the detect block into three distinct paths, each specialized in detecting objects of different sizes.
Each path consists of multiple convolutional layers and concat operations, which progressively reduce the resolution of feature maps, ensuring proper handling of objects at different scales.

## Slide 15
YOLOv10 Architecture
Elimination of the NMS (Non-Maximum Suppression) post-processing step during training.
Holistic approach to optimize every component of the model
Partial Self-Attention (PSA) module

## Slide 16
Experimental Setup and Analysis Conducted
Environment
Hyperparameter tuning
CO2 Emissions
Inference Evaluation
Optimization
Results and Discussion
Future Works

## Slide 17
Environment
Robust experimental environment given by a Docker container, to provide a consistent and isolated platform for conducting our experiments.
Computational capabilities of an Intel(R) Xeon(R) Gold 6254 CPU @ 3.10GHz and GPU type NVIDIA RTX A6000 for our trainings.

## Slide 18
Hyperparameter tuning
Conducted tests
Tested Parameters:
Batch size
Optimizer
Number of Epochs
Learning Rate
Momentum
Weight Decay
Warmup
Hyperparameter tuning for YOLOv8s and YOLOv10s architectures.
This involved iteratively adjusting key parameters to maximize the models' detection accuracy and efficiency.

## Slide 19
Hyperparameter tuning
Results
( epochs: 200, batch size: 64, optimizer: SGD, lr: 0.010, wd: 0.0005, wu: 3, mom: 0.9)
Time avg v8: 8h
Time avg v10: 10h

## Slide 20
Hyperparameter tuning
CO2 Emissions
YOLOv8s with the best configuration emitted 1.82 Kg of CO2.
YOLOv10s with the best configuration emitted 2.23 Kg of CO2
driving 9 km with a car
Charging a smartphone 11 times

## Slide 21
Inference
Results
We tested the inference on both YOLOv8 and YOLOv10 using 3 samples.
YOLOv8s
YOLOv10s
Input sample
Time avg: 2.5s

## Slide 22
Inference
Explainability
Eigen CAM: technique applied in neural networks to generate an activation map that highlights the regions of an image that have most influenced the model's prediction.
YOLOv8s
YOLOv10s
RED for the areas that influenced the most
BLUE for the areas of less importance
Bounding box and relative Confidence Score

## Slide 23
Optimization
YOLOv8s architecture’s modifications
Deleted Layers
Small Objects Detection block
Layer-based pruning approach

## Slide 24
Optimization: YOLOv8s architecture for Small Objects

## Slide 25
Optimization
YOLOv8 Architecture’s file modifications
We have commented out the file’s rows corrisponding to the layers we wanted to delete.

## Slide 26
Optimization
YOLOv8s Results
Reduction of approximately 18%, 5462 seconds less!
The YOLOv8 Small Custom configuration offers a clear advantage in terms of time efficiency, with a significant reduction in execution times, at the cost of a minimal penalty in performance.
Tradeoff between Speed and Accuracy

## Slide 27
Optimization
YOLOv10s Modifications
The procedure for YOLOv10s is the same of YOLOv8s procedure, taking into account the slight architectural differences between the two models.
Deleted Layers

## Slide 28
Optimization
YOLOv10 Architecture’s file modifications

## Slide 29
Optimization
YOLOv10s Results

## Slide 30
Results and Discussion
The results obtained have shown significant improvements in terms of precision and efficiency compared to previous versions.
Our analysis of CO2 suggests that computational efficiency must be balanced with the need to reduce the carbon footprint.
We found a tradeoff between speed and accuracy through our customized architecture for small objects.

## Slide 31
Future Works
Using a MobileNet as a convolutional backbone could significantly increase the computational efficiency
Approach the task not only as a detection task but also as a classification task
Focus on developing energy-efficient training protocols and optimizing the computational resources required for both training and inference.

## Slide 32
Thank You for the Attention
Zazzarini Micol
Fiorani Andrea

## Slide 33
YOLOv8 architecture
blocks
Architecture’s blocks:
C2f
Bottleneck
SPPF
Conv
Detect
MODEL VARIANTS

## Slide 34
YOLOv8 architecture
Backbone
The backbone is responsible for feature extraction from the input image
Composed by:
Conv layers
C2f blocks
SPPF block

## Slide 35
YOLOv8 architecture
Neck
The neck is responsible for integrating information from various resolution scales.
Composed by:
C2f blocks
Concat blocks
Conv layers
Upsample blocks

## Slide 36
Hyperparameter tuning
Results

## Slide 37
Inference
Examples